## Slide 1
Final Pitch Tracks
  Experiments with the Keele Database (British English )
  10 phonetically balanced sentences spoken by 5 male and 5 female English speakers. Manually checked reference pitch was used.
  Experiments with the TIMIT Database (American English)
  20 speakers (10 male and 10 female) were selected with 5 sentences from each speaker, resulting in a total of 100 sentences
  The clean YAAPT pitch track was used as the reference. *: the YAAPT voiced/unvoiced decisions were applied to RAPT and YIN
  Experiments with the RASC863 Database (Mandarin Chinese)
  A total of 1065 sentences from 6 speakers (3 male and 3 female) were selected.
  The clean YAAPT pitch track was used as the reference. *: the YAAPT voiced/unvoiced decisions were applied to RAPT and YIN
  Experimental Setup
  Tracking Algorithms
  YIN (de Cheveigne and Kawahara, 2002)
  A modified version of the autocorrelation method
  No voiced/unvoiced decision
  RAPT (Talkin, 1995)
  MATLAB version of Normalized Cross Correlation Function (NCCF)
  PRAAT (Boersma and Weenink, 2001)
  The autocorrelation method is used in this speech analysis tool
  Evaluation Method
  Additive background noise
  No additional noise added (clean)
  5 dB white noise 1(W -5)
  4 dB babble noise (B-5)
  Simulated telephone speech
  a SRAEN (300-3400 Hz FIR bandpass) filter
  Error measures
  Gross Error
  The percentage of the estimated pitch frames deviating significantly (20%) from the reference
  All frames are considered as voiced
  Big error
  Gross error and voiced/unvoiced decision error are included
An Experimental Comparison of Fundamental Frequency Tracking Algorithms
Hongbing Hu* and Stephen A. Zahorian
Department of Electrical and Computer Engineering, Binghamton University * Currently Intel Corporation
Binghamton, NY 13902, USA
Hongbing.hu@binghamton.edu, Zahorian@binghamton.edu
Introduction
  “Yet Another Algorithm for Pitch Tracking -YAAPT” (Zahorian and Hu, 2008) provides highly accurate and noise robust fundamental frequency (F0) tracking for both studio quality speech and telephone speech
  Further more work has been done to improve the algorithm and especially to improve its functionality and ease of use as MATLAB functions
  The current YAAPT is experimentally compared with YIN, PRAAT, and RAPT with multiple databases including American English (TIMIT), British English (Keele), and Mandarin Chinese (RASC863)
YAAPT MATLAB Function
[Pitch, frms, rate] = yaapt(Data, Fs, VU, ExtrPrm, fig)
  Example
  Read data from the sample sample/ f1nw0000.wav file.
  Compute the pitch track with the yaapt( ) function. The computed pitch is saved in an array Pitch of length nf.
  Plot the computed pitch track.
  Online Download
  http://www.ws.binghamton.edu/zahorian/yaapt.htm
YAAPT Pitch Tracking
  Nonlinear processing : the squared value of the speech is used to restore missing fundamentals
  F0 track calculation from the spectrogram: a spectral F0 track is estimated using Spectral Harmonics Correlation (SHC) from the spectrogram of the nonlinear processed signal
  F0 candidate estimation: candidates are extracted based on the NCCF (Normalized Cross Correlation Function) in the time domain
  Final F0 determination: dynamic programming is applied to arrive at a final F0 track
  Voiced/Unvoiced Decision: a normalized low frequency energy ratio (NLFER) function is proposed
 | Studio |  |  | Simulated telephone |  | 
Method | Clean | W-5 | B-5 | Clean | W-5 | B-5
YAAPT | 3.08 | 3.77 | 8.48 | 4.23 | 6.21 | 28.66
PRAAT | 3.35 | 6.91 | 15.98 | 9.91 | 15.72 | 32.56
RAPT | 8.24 | 21.33 | 18.04 | 9.5 | 18.21 | 29.09
YIN | 3.23 | 4.85 | 14.74 | 20.9 | 25.96 | 37.4
  Conclusions
  YAAPT shows better performance than the other fundamental frequency trackers for most conditions
  YAAPT is available as a standalone MATALB function with various options and features
  References
[1] Zahorian, S. A., and Hu, H. (2008). "A Spectral/temporal method for Robust Fundamental Frequency Tracking," J. Acoust. Soc. Am. 123 (6)
[2] de Cheveigne, A., and Kawahara, H. (2002). "YIN, a fundamental frequency estimator for speech and music," J. Acoust. Soc. Am. 111(4)
[3] Talkin, D. (1995). “A robust algorithm for pitch tracking (RAPT),” in Speech Coding and Synthesis, pp. 495–518.
[4] Boersma, P., and Weenink, D. (2001). “PRAAT, a system for doing phonetics by computer,” Glot International 5(9/10), 341-345.
 | Studio |  |  | Simulated telephone |  | 
Method | Clean | W-5 | B-5 | Clean | W-5 | B-5
YAAPT | 6.09 | 7.99 | 22.44 | 14.07 | 16.89 | 44.39
PRAAT | 8.64 | 19.87 | 34.9 | 12.83 | 20.12 | 46.9
RAPT | No voiced/unvoiced decision |  |  |  |  | 
YIN | No voiced/unvoiced decision |  |  |  |  | 
Processing Illustration
 | Studio |  |  | Simulated telephone |  | 
Method | Clean | W-5 | B-5 | Clean | W-5 | B-5
YAAPT | 0.00 | 0.39 | 0.46 | 0.99 | 0.74 | 0.90
PRAAT | 18.19 | 18.02 | 18.08 | 18.41 | 18.19 | 18.33
RAPT | 3.04 | 2.85 | 2.91 | 3.26 | 3.03 | 3.17
YIIN | 0.39 | 0.20 | 0.26 | 0.61 | 0.36 | 0.52
 | Studio |  |  | Simulated telephone |  | 
Method | Clean | W-5 | B-5 | Clean | W-5 | B-5
YAAPT | 0.00 | 4.77 | 21.77 | 10.49 | 14.80 | 47.77
PRAAT | 13.47 | 12.28 | 28.73 | 20.16 | 21.89 | 53.00
RAPT* | 4.98 | 7.15 | 24.21 | 13.10 | 16.63 | 49.03
YIN* | 2.78 | 5.31 | 22.51 | 10.88 | 15.06 | 48.69
 | Studio |  |  | Simulated telephone |  | 
Method | Clean | W-5 | B-5 | Clean | W-5 | B-5
YAAPT | 0.00 | 0.18 | 0.18 | 0.46 | 0.29 | 0.34
PRAAT | 4.04 | 3.91 | 3.90 | 4.17 | 4.01 | 4.05
RAPT | 0.17 | 0.04 | 0.03 | 0.31 | 0.14 | 0.19
YIN | 0.16 | 0.03 | 0.02 | 0.30 | 0.13 | 0.18
 | Studio |  |  | Simulated telephone |  | 
Method | Clean | W-5 | B-5 | Clean | W-5 | B-5
YAAPT | 0.00 | 9.94 | 27.14 | 13.22 | 17.84 | 40.58
PRAAT | 21.18 | 19.80 | 35.76 | 30.82 | 30.68 | 49.37
RAPT* | 4.14 | 12.35 | 29.41 | 16.17 | 20.00 | 41.08
YIN* | 2.18 | 10.92 | 28.37 | 14.43 | 18.80 | 41.50
INPUTS |  | 
Data | Input speech acoustic samples | 
Fs | Sampling rate of the input data | 
VU | Whether to make voiced/unvoiced decisions (optional) | 
ExtrPrm | Additional parameters for performance control (optional) | 
fig | plot pitch tracks, spectrum, energy, etc (optional) | 
OUTPUTS |  | 
Pitch |  | Final pitch track in Hz. Unvoiced frames are 0s.
frms |  | Total number of calculated frames, or the length of output pitch track
rate |  | Frame rate of output pitch track in ms
>> [Data, Fs] = wavread ('sample/f1nw0000.wav');
>> [Pitch, nf] = yaapt(Data, Fs);
>> plot(Pitch, ‘.-‘);
Speech Communication Lab, State University of New York at Binghamton
Big Error
Gross Error
Gross Error
Big Error
Gross Error
Big Error
Figure from ref Zahorian and Hu, 2008